## Slide 1
NIA ENGINEERING
I&C Common solutions – IA02
9 October 2024
Prepared by:
I. Smirnov, N. Babinov, A. Govorov

## Slide 2
Agenda
Brief introduction | 
Idea of common solution | 
Currently available and planned common solutions | 
How to integrate a common solution into an existing project | 
Conclusion | 
Number of slides - 20
Duration of the presentation ~ 15 min
NIA ENGINEERING

## Slide 3
OUR TEAM AND RESPONSIBILITY
Our responsibility
V&V activities – inspection of SMS, MIP, wiring diagrams, software and on-site manufacturing
Preparation of manufacturing progress reports
Preparation of the common solutions
Arthur Leveque – IO RO
Nikita Babinov – General manager of NIA Engineering
Alexey Govorov – Technical coordinator of NIA team
NIA ENGINEERING
Responsible organizations
Ilya Smirnov – RAWE Project Manager

## Slide 4
IDEA OF COMMON SOLUTION
NIA ENGINEERING
Solution (A) prepared by the I&C team that potentially can be used by other I&C teams
Integration of the solution (A) into I&C project taking into account specific for this I&C project PBS and CBS
Common solution package
I&C project where solution (A) can be used

## Slide 5
BENEFITS OF COMMON SOLUTIONS
FOR I&C PRODUCTION TEAMS
NIA ENGINEERING
Decrease of the production time
More attention can be paid to the complex parts of the I&C project
Ready for use solution
Clear parameters of HW and SW
Automation of a significant part of the integration process

## Slide 6
EXISTING COMMON SOLUTIONS
NIA ENGINEERING
List of Common solution that are defined today
Thermocouple monitoring [AFPCTH]
Mirror Cleaning Operation Scheme [AFPL4Q]
Temperature control through Baking Jacket [AFPLNZ]
Piezo motor controller [B5VN3U]
Imaging System
ADC with FPGA in μTCA form factor
Being updated according to new prototype prepared by 55.E6 team
These common solutions will be prepared later in the project
Elements of the Common solution package:
  Guideline for implementation
  FBS/NDS generation tool
  FBS/NDS specification
  BOM if applicable
  Set of HMI objects

## Slide 7
THERMOCOUPLE MONITORING SYSTEM
NIA ENGINEERING
Purpose
Almost all diagnostic systems will need to monitor temperature at various locations. The goal of this package is to provide an existing solution with a slow controller that can be quickly adapted to all systems.
Hardware used
This solution uses the Siemens S7-1500 slow controller.
More information about Hardware used can be found in the FBS specification for thermocouple monitoring system [ADAVQH]
Communication scheme of the 55.Q0 solution for thermocouple monitoring system

## Slide 8
MIRROR CLEANING
OPERATION SCHEME
NIA ENGINEERING
Purpose
Each Diagnostic operator will monitor the status of their System mirrors and decide when a mirror cleaning request shall be issued. The Main Diagnostic Operator will collect all requests from the individual systems and provide a unique consolidated request to get a Tokamak Operation slot.
There is no Hardware used in this common solution
All the variables are deployed on PSH
Main HMI screen for Mirror cleaning prepared by the Cosylab team

## Slide 9
TEMPERATURE CONTROL THROUGH BAKING JACKET
NIA ENGINEERING
Purpose
Several Diagnostics systems need to control the temperature of some of their pipes to follow the Temperature of the vacuum.
Hardware used
There are 2 COTS controllers used in the solution:
EPC2000 Temperature controller
EPACK Heating Power controller
Main HMI screen for Temperature control through Backing Jacket prepared by the 55.G3.50 team
EPC2000
EPACK

## Slide 10
PIEZO MOTOR
CONTROLLER
NIA ENGINEERING
Purpose
To provide a fully CODAC-integrated solution for Piezo motor controller.
Hardware used
Piezo motor controller Newport 8742 is used in this common solution.
HMI screens for setting and controlling piezo motor controller Newport 8742

## Slide 11
HOW TO INTEGRATE COMMON SOLUTION INTO EXISTING PROJECTS - GENERAL APPROACH
NIA ENGINEERING
Download the Common solution package from IDM
Generate FBS/NDS templates
Actions to be performed on Windows environment
Import into existing FBS/NDS templates
Import FBS/NDS template into EA project
Convert EA project to .xml using EA2SDD script
Import .xml into SDD project
Generate configuration file
Import the .opi files into CS project
Change the common macros to specific data for the I&C project
Run the SDD project and test the HMI with integrated common solution
Actions to be performed on CODAC environment

## Slide 12
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 1
NIA ENGINEERING
For demonstration Temperature control through Backing Jacket is used
FBS/NDS generation using FBS_template_for_Temperature_Control_Com_ARXHPQ_v1_0.xlsm [ARXHPQ]

## Slide 13
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 1
NIA ENGINEERING
For demonstration Temperature control through Backing Jacket is used
FBS/NDS generation using FBS_template_for_Temperature_Control_Com_ARXHPQ_v1_0.xlsm [ARXHPQ]

## Slide 14
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 2
NIA ENGINEERING
Generated FBS template ready for integration

## Slide 15
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 3
NIA ENGINEERING

## Slide 16
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 4
NIA ENGINEERING
NDS variables EPACK and EPC2000 for Temperature Control Common Solution [AU3RWH]

## Slide 17
NDS variables EPACK and EPC2000 for Temperature Control Common Solution [AU3RWH]
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 4
NIA ENGINEERING

## Slide 18
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 5
NIA ENGINEERING
Generated NDS template

## Slide 19
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 6
NIA ENGINEERING
Importing into EA project
Using the standard procedure for importing data into EA project through the “Functional analysis” EA Add-in

## Slide 20
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 7
NIA ENGINEERING
Importing generated .xml file into SDD
Standard procedure to import and run the project:
Prepare the .xml file using the ea2sdd script
Import .xml into SDD
Run the SDD from Maven Editor on target deployment units

## Slide 21
HOW TO INTEGRATE COMMON SOLUTION INTO AN EXISTING PROJECT STEP 8
NIA ENGINEERING
Importing the .opi files into CS project

## Slide 22
CONCLUSION
NIA ENGINEERING
Please give us your feedback after using the Common solution on our Confluence page:
https://confluence.iter.org/x/GJ9MJw
Arthur Leveque: arthur.leveque@iter.org
Ilya Smirnov: ilya.smirnov@rosatom.fr
Nikita Babinov: n.babinov@niaengineering.ru
Alexey Govorov: a.govorov@niaengineering.ru
If you have questions or suggestions to improve our Common solution, feel free to contact us